VIM1 Install OS into eMMC on Ubuntu
https://docs.khadas.com/products/sbc/vim1/install-os/install-os-into-emmc-on-ubuntu
sudo apt-get install libusb-dev git parted
$ git clone https://github.com/khadas/utils
Or just pull it (if you have already cloned this repository).

$ cd /path/to/utils
$ git pull
Install the Flash Tool
You need to install USB rules and create some links.

$ cd /path/to/utils
$ sudo ./INSTALL

You must now put your board into Upgrade Mode.
https://docs.khadas.com/products/sbc/vim1/install-os/boot-into-upgrade-mode#tab__serial-mode

Connect VIM1 to PC with a USB-C cable.
Quickly press the Function key 3 times in 2 seconds, then release the key. You will see the Power LED (Blue) blink for about 3 seconds.
After the Power LED (Blue) turns OFF, this indicates that the board is in Upgrade Mode (Maskrom Mode).

or

Power on VIM1.
Long press the POWER key without releasing it.
Short press the Reset key and release it.
Count for 2 to 3 seconds, then release the POWER key to enter into Upgrade Mode. You will see the sys-led turn ON when you’ve entered Upgrade Mode.

$ lsusb | grep Amlogic
Bus 003 Device 073: ID 1b8e:c004 Amlogic, Inc. DNL

burn-tool -v aml -b VIM1 -i /path/to/image

For more information please refer to flash-tool docs.

# VIM1 Build Ubuntu
https://dl.khadas.com/.images/vim1/
https://dl.khadas.com/firmware/vim1/ubuntu/emmc/
https://docs.khadas.com/products/sbc/vim1/development/linux/build-ubuntu

WiFi
RTL8821CE driver
sshfs
sshfs khadas@192.168.100.4:/home/khadas/aqua /home/user/SOFT/Github/Sublime_tests/Khadas_aqua

https://khadas.github.io/linux/edge/WiringPi.html

gpio readall

C Program Usage
Get demo source code
$ wget https://dl.khadas.com/development/code/docs_source/wiringpi.c
Compile
$ g++ -o wiringpi wiringpi.cpp -lwiringPi -lpthread -lrt -lm -lcrypt
$ sudo ./wiringpi
wPi Pin 1 now is GIGH
wPi Pin 1 now is LOW
wPi Pin 1 now is GIGH
wPi Pin 1 now is LOW

I2C
I2C A
Sensor SCL <-> I2C_SCK_A (PIN 22)
Sensor SDA <-> I2C_SDA_A (PIN 23)
Sensor GND <-> GND
Sensor VCC <-> 5V or 3.3V //depends on external device power requirement
I2C B
Sensor SCL <-> I2C_SCK_B (PIN 25)
Sensor SDA <-> I2C_SDA_B (PIN 26)
Sensor GND <-> GND
Sensor VCC <-> 5V or 3.3V //depends on external device power requirement

i2cdetect -y -r 1

Read the Value of the Device Register
Read the device connected to the I2C A bus, whose device address is 0x1d and register address is 0x0d.

# i2cget -f -y 1 0x1d 0x0d

sudo apt-get install libi2c-dev

https://github.com/khadas/WiringPi.git

gpio i2cdete

1Wire

https://docs.khadas.com/products/sbc/vim1/applications/gpio/1wire

VIM1/2	37	GPIOH_5

Edit /boot/env.txt to add the onewire node to overlays node if it doesn't exist.

overlays=onewire

Reboot the system for this change to take effect.

Get Sensor Data
Here we attach a 1-Wire device DS18B20 temperature sensor to the 1-Wire bus.

Enter the driver directory:

khadas@Khadas:~$ cd /sys/bus/w1/devices
khadas@Khadas:/sys/bus/w1/devices$ ls
28-0119395ebf91 w1_bus_master1
You can see the node of ds18b20 is 28-0119395ebf91. Enter this directory:

khadas@Khadas:/sys/bus/w1/devices$ cd 28-0119395ebf91
khadas@Khadas:/sys/bus/w1/devices/28-0119395ebf91$ ls
driver id name power subsystem uevent w1_slave
Read w1_slave file will get the temperature value:

khadas@Khadas:/sys/bus/w1/devices/28-0119395ebf91$ cat w1_slave
b1 01 4b 46 7f ff 0c 10 d8 : crc=d8 YES
b1 01 4b 46 7f ff 0c 10 d8 t=27062
Disable 1-Wire to Use GPIO
If you want to use normal GPIO instead of 1-Wire, you can remove the 1-Wire node in Device Tree Overlay.

gpio mode 10 OUT
gpio write 10 1

PIN22 gpio 6 Резерв
PIN23 gpio 7 COLD
PIN29 gpio 10 LAMP
PIN30 gpio 11 HEAT
PIM31 gpio 12 POMPA
PIM32 gpio 13 Воздух
PIM35 gpio 15 FOOD

PIN37 onewire измерение температуры
PIN40 GND
PIN1 +5
PIN2 +5

cat /sys/bus/w1/devices/28-011920f5f0d0/w1_slave
more /sys/bus/w1/devices/*/w1_slave

Автозагрузка программы
достаточно создать простой юнит-файл и добавить его в автозагрузку, как любой другой сервис. Сначала создадим этот файл:

cd /lib/systemd/system
sudo nano aqua.service

[Unit]
Description=aquarium Service
After=multi-user.target
[Service]
Type=idle
ExecStart=/home/khadas/aqua/aqua
[Install]
WantedBy=multi-user.target

sudo chmod 644 /lib/systemd/system/aqua.service

Затем обновить конфигурацию и добавить в автозагрузку Linux новый скрипт:
 sudo systemctl daemon-reload
sudo systemctl enable aqua.service