### Making a Beaglebone Black always boot from the Micro-SD
Using the "hold down the button" method described above, the board will boot and reboot from the Micro-SD until power is removed. After the next power cycle it will return to booting from the eMMC. The ROM code in the AM335x chip actually boots from the first FAT partition it finds that has the active flag set. It looks first on the eMMC, then on the Micro-SD. To make the board always boot from the Micro-SD slot instead of the onboard eMMC, first boot FreeBSD by holding down the boot button as described above. After booting, log on as root and turn off the active/bootable flag on the eMMC FAT partition:
Using the "hold down the button" method described above, the board will boot and reboot from the Micro-SD until power is removed. After the next power cycle it will return to booting from the eMMC. The ROM code in the AM335x chip actually boots from the first FAT partition it finds that has the active flag set. It looks first on the eMMC, then on the Micro-SD. To make the board always boot from the Micro-SD slot instead of the onboard eMMC, first boot FreeBSD by holding down the boot button as described above. After booting, log on as root and turn off the active/bootable flag on the eMMC FAT partition:
gpart unset -a active -i 1 mmcsd1
To restore the board to booting from the eMMC do:
gpart set -a active -i 1 mmcsd1
## GPIO
Default settings for P8 and P9 expansion headers (LCD/HDMI pins are missing).
P9				BeagleBoneBlack	P8
DGND	1	2	DGND		DGND	1	2	DGND
VDD_3V3	3	4	VDD_3V3		MMC1_DAT6 (GPIO_38)	3	4	MMC1_DAT7 (GPIO_39)
VDD_5V	5	6	VDD_5V		MMC1_DAT2 (GPIO_34)	5	6	MMC1_DAT3 (GPIO_35)
SYS_5V	7	8	SYS_5V		GPIO_66	7	8	GPIO_67
PWR_BTN	9	10	SYS_RESET		GPIO_69	9	10	GPIO_68
GPIO0_30	11	12	GPIO1_28		GPIO_45	11	12	GPIO_44
GPIO0_31	13	14	PWM1A (GPIO1_8)		PWM2B (GPIO0_23)	13	14	GPIO_26
GPIO1_16	15	16	PWM1B (GPIO1_19)		GPIO_47	15	16	GPIO_46
I2C1_SCL (GPIO0_4)	17	18	I2C1_SDA (GPIO0_5)		GPIO0_27	17	18	GPIO_65
I2C2_SCL (GPIO0_13)	19	20	I2C2_SDA (GPIO0_12)		PWM2A (GPIO0_22)	19	20	MMC1_CMD (GPIO_63)
GPIO0_3	21	22	GPIO0_2		MMC1_CLK (GPIO_62)	21	22	MMC1_DAT5 (GPIO_37)
GPIO1_17	23	24	GPIO0_15		MMC1_DAT4 (GPIO_36)	23	24	MMC1_DAT1 (GPIO_33)
GPIO3_21	25	26	GPIO0_14		MMC1_DAT0 (GPIO_32)	25	26	GPIO_61
GPIO3_19	27	28	SPI1_CS0 (GPIO3_17)		GPIO_86	27	28	GPIO_88
SPI1_MISO (GPIO3_15)	29	30	SPI1_MOSI (GPIO3_16)		GPIO_87	29	30	GPIO_89
SPI1_CLK (GPIO3_14)	31	32	VDD_ADC (1.8V)		GPIO0_10	31	32	GPIO0_11
AIN4	33	34	GNDA_ADC		GPIO0_9	33	34	GPIO_81
AIN6	35	36	AIN5		GPIO0_8	35	36	GPIO_80
AIN2	37	38	AIN3		GPIO_78	37	38	GPIO_79
AIN0	39	40	AIN1		GPIO_76	39	40	GPIO_77
GPIO0_20	41	42	SPI1_CS1 (GPIO0_7)		GPIO_74	41	42	GPIO_75
DGND	43	44	DGND		GPIO_72	43	44	GPIO_73
DGND	45	46	DGND		GPIO_70	45	46	GPIO_71

## Anatomy of a BeagleBone Boot Image
(This information applies to both the older white BeagleBone and the newer BeagleBone Black.)
The FreeBSD bootable image for BeagleBone is an MBR-partitioned image with FAT and UFS partitions containing the following files:
- FAT Partition
  - MLO - First stage boot, from U-Boot
  - BB-uboot.img - Second stage: U-Boot
  - BB-uEnv.txt - configuration for U-Boot
  - BBONE.DTB - Binary FDT, loaded by U-Boot
  - BBONE.DTS - Source FDT for reference
  - BBONEBLK.DTB - Binary FDT used on BeagleBone Black
  - BBONEBLK.DTS - Source FDT for reference
  - BBubldr - Third stage: FreeBSD bootloader
- UFS Partition
  - /boot/kernel - FreeBSD kernel
  - ... rest of FreeBSD ...
The boot process works like this:
- AM3358 SoC ROM code inspects the MicroSDHC card, finds the MBR partition table and loads "MLO" from the first FAT partition. MLO is loaded before external RAM is initialized, so it has to be under 110k to fit within the on-chip RAM. MLO here is a stripped-down version of U-Boot.
- MLO loads BB-UBOOT.IMG from the first FAT partition. U-Boot is a highly modular boot loader system that can be used on a wide variety of systems. The loader is configured with built-in script commands that can be partially overridden by additional commands in the BB-uEnv.txt file.
- U-Boot loads BB-uEnv.txt and follows those commands to load BBubldr at address 0x88000000. ubldr is a variant of FreeBSD's standard loader(8) program that is designed to be chain-loaded from U-Boot. It calls into U-Boot for low-level device access, which allows ubldr to load FreeBSD on any system that supports U-Boot.
- ubldr locates the UFS partition, loads /boot/kernel/kernel from UFS to address 0x80200000 and executes it.
Note: Except for MLO, which must have exactly that name in order to be found and loaded by the ROM code, all the FAT partition boot files named above begin with "BB." This convention is used by the Crochet build tool to allow more than one boot system to reside on the same disk image. FreeBSD images built by other means may not follow this convention.